## Slide 1: Atlantic Woodworkers’ Association Virtual sessions
September 2021

## Slide 2: Agenda Meeting format - review Safety Second - Calum Tech/ Text/ Tools - Darryl/Stephen/Brad Short Cuts - Brad AWA Primetime - none Show and Tell / Challenge - What did you make this summer? Final Word - December meeting comes up fast

## Slide 3: Mortise & Tenon joinery: Drawboring
Brad Holley
Drawboring mechanically reinforces a typical M&T join using an offset wooden peg
The join pre-dates the use of clamps
Useful now in applications where clamps might not be long enough and/or sufficient on their own

## Slide 4
MORTISE & TENON JOINERY: DRAWBORING
A hole matching the diameter of the peg is first drilled through the mortise piece - typically ½” or more from the edge
Holes can be offset from one-another to avoid splitting along the grain
The location of that hole is then transferred to the tenon piece using just the brad point

## Slide 5
MORTISE & TENON JOINERY: DRAWBORING
The mark is moved slightly towards the shoulder of the tenon (1/16” is often enough)
A sharpened peg is driven through the hole which pulls the join in tight (aided by a drawbore pin
The pin actually bends as it goes through the offset hole

## Slide 6
MORTISE & TENON JOINERY: DRAWBORING
After the pin is driven through the joint, it is cut flush to the surface of the piece and sanded clean
Paul Sellers has a YouTube post about this technique: https://www.youtube.com/watch?v=iblkJnlmg4w
See also article by Christopher Schwarz in Popular Woodworking Autumn 2005, 12-15

## Slide 7
MORTISE & TENON JOINERY: DRAWBORING
Applications: permanent joins found in:
Windows and doors
Frames
Leg to apron joins
Timber framing

## Slide 8: Tech/ Text/ Tools

## Slide 9: Short Cuts - Sprung Joints
“Springing” a glue joint - such as for a table top or panel, by planing a slight cove makes for tighter joins

## Slide 10: Tighter glue lines - Sprung Joints
With your stock already prepped - plane a slight cove along the length of the glue edges
Start in the middle with short, shallow pass
A few progressively longer strokes
A slight gap will appear when aligning the edges while the ends squarely touch
Handy when you have few clamps